## Slide 1: Effects of Contention on Message Latencies in Large Supercomputers
Abhinav S Bhatele and Laxmikant V Kale
ACM Research Competition, SC ‘08
IS TOPOLOGY IMPORTANT AGAIN?

## Slide 2: Outline
Why should we consider topology aware mapping
for optimizing performance?
Demonstrate the effects of contention on
message latencies through simple MPI benchmarks
Obtaining topology information: TopoManager API
Case Study: OpenAtom

## Slide 3: The Mapping Problem
Given a set of communicating parallel “entities”, map them onto physical processors
Entities
  COMM_WORLD ranks in case of an MPI program
  Objects in case of a Charm++ program
Aim
  Balance load
  Minimize communication traffic

## Slide 4: Target Machines
3D torus/mesh interconnects
Blue Gene/P at ANL:
  40,960 nodes, torus - 32 x 32 x 40
XT4 (Jaguar) at ORNL:
  8,064 nodes, torus - 21 x 16 x 24
Other interconnects
  Fat-tree
  Kautz graph: SiCortex

## Slide 5: Motivation
Consider a 3D mesh/torus interconnect
Message latencies can be modeled by
(Lf/B) x D + L/B
Lf = length of flit, B = bandwidth,
D = hops, L = message size
When (Lf * D) << L, first term is negligible
But in presence of contention …

## Slide 6: MPI Benchmarks†
Quantification of message latencies and dependence on hops
  No sharing of links (no contention)
  Sharing of links (with contention)
† http://charm.cs.uiuc.edu/~bhatele/phd/contention.htm

## Slide 7: WOCON: No contention
A master rank sends messages to all other ranks, one at a time (with replies)

## Slide 8: WOCON: Results
ANL Blue Gene/P
ORNL XT4
PSC XT3
(Lf/B) x D + L/B

## Slide 9: WICON: With Contention
Divide all ranks into pairs and everyone sends to their respective partner simultaneously
Near Neighbor: NN
Random: RND

## Slide 10: WICON: Results
ANL Blue Gene/P
PSC XT3
Notes: BG/P = 1.737 times
XT3 = 2.24 times

## Slide 11: Message Latencies and Hops
Pair each rank with a partner which is ‘n’ hops away

## Slide 13: Results
8 times
Notes: 1 to 2 – 1.84
1 to 3 – 2.11
1 to 4 - 2.55
1 to 7 – 3.54
1 to 8 – 7.396

## Slide 14
Notes: Peak bandwidth of each link = 425 MB/s unidirectional

## Slide 15: Difference from previous work
Then | Now
Mainly for theoretical object graphs on hypercubes, shuffle exchange and other theoretical networks | Object graphs from real applications on 3D torus/mesh topologies
Most techniques were used offline – slow | Fast, runtime solutions
Demonstrated on graphs with 10-100 nodes | Scalable techniques for large machines
No cardinality variation | Multiple objects per processor
Not tested with real applications on actual machines – theoretical work | Targeted at production codes – tested with real applications

## Slide 16: Difference from recent work
[5] G. Bhanot, A. Gara, P. Heidelberger, E. Lawless, J. C. Sexton, and R. Walkup. Optimizing task layout on the Blue Gene/L supercomputer. IBM Journal of Research and Development, 49(2/3), 2005.
  Use of simulated annealing – slow and solution is developed offline
[6] Hao Yu, I-Hsin Chung, and Jose Moreira. Topology mapping for Blue Gene/L supercomputer. In SC '06: Proceedings of the 2006 ACM/IEEE conference on Supercomputing, page 116, New York, NY, USA, 2006. ACM
  Node mappings for simple scenarios (1D rings, 2D meshes, 3D)
  Only useful in case of simple near-neighbor communication

## Slide 17: Topology Manager API†
The application needs information such as
  Dimensions of the partition
  Rank to physical co-ordinates and vice-versa
TopoManager: a uniform API
  On BG/L and BG/P: provides a wrapper for system calls
  On XT3 and XT4, there are no such system calls
    Help from PSC and ORNL staff to discovery topology at runtime
  Provides a clean and uniform interface to the application
† http://charm.cs.uiuc.edu/~bhatele/phd/topomgr.htm
Notes: This can be used by MPI Topology functions

## Slide 18: OpenAtom
Ab-Initio Molecular Dynamics code
Communication is static and structured
Challenge: Multiple groups of objects with conflicting communication patterns

## Slide 19: Parallelization using Charm++
[10] Eric Bohm, Glenn J. Martyna, Abhinav Bhatele, Sameer Kumar, Laxmikant V. Kale, John A. Gunnels, and Mark E. Tuckerman. Fine Grained Parallelization of the Car-Parrinello ab initio MD Method on Blue Gene/L. IBM J. of R. and D.: Applications of Massively Parallel Systems, 52(1/2):159-174, 2008.

## Slide 20
Planes
Planes
States
Planes
States
GSpace
RealSpace
PairCalculator

## Slide 21: Topology Mapping of Chare Arrays
State-wise
communication
Plane-wise
communication
Joint work with Eric J. Bohm

## Slide 22: Results on Blue Gene/P (ANL)
Chart: No. of cores
| 1024 | 2048 | 4096 | 8192
w256 Default BG/P | 10.78 | 6.85 | 4.21 | 3.52
w256 Topology BG/P | 6.7 | 3.77 | 2.17 | 1.77

## Slide 23: Results on XT3 (BigBen)
Chart: No. of cores
| 512 | 1024 | 2048
w256 Default XT3 | 7.5 | 5.7 | 3.94
w256 Topology XT3 | 6.58 | 4.14 | 2.43

## Slide 24: Summary
Topology is important again
Even on fast interconnects such as Cray
In presence of contention, bandwidth occupancy effects message latencies significantly
Increases with the number of hops each message travels
Topology Manager API: A uniform API for IBM and Cray machines
Case Studies: OpenAtom, NAMD, Stencil
Eventually, an automatic mapping framework

## Slide 25: Acknowledgements: 1. Argonne National Lab: Pete Beckman, Tisha Stacey 2. Pittsburgh Supercomputing Center: Chad Vizino, Shawn Brown 3. Oak Ridge National Laboratory: Patrick Worley, Donald Frederick 4. IBM: Robert Walkup, Sameer Kumar 5. Cray: Larry Kaplan 6. SiCortex: Matt Reilly
References: 1. Abhinav Bhatele, Laxmikant V. Kale, Dynamic Topology Aware Load Balancing Algorithms for MD Applications, submitted to Philosophical Transactions of the Royal Society A, 2008
2. Abhinav Bhatele, Laxmikant V. Kale, Benefits of Topology-aware Mapping for Mesh Topologies, LSPP special issue of Parallel Processing Letters, 2008
3. Abhinav Bhatele, Laxmikant V. Kale, Application-specific Topology-aware Mapping for Three Dimensional Topologies, Proceedings of Workshop on Large-Scale Parallel Processing (held as part of IPDPS '08), 2008