## Slide 1: Automating Topology Aware Task Mapping on Large Parallel Machines
Abhinav S Bhatele
Advisor: Laxmikant V. Kale
University of Illinois at Urbana-Champaign

## Slide 2: Current Machines and their Topologies
3D Mesh – Cray XT3/4/5
3D Torus – Blue Gene/L, Blue Gene/P
Fat-tree, CLOS network – Infiniband, Federation
Kautz Graph – SiCortex
Future Topologies – Blue Waters, Blue Gene/Q?
Notes:   Hypercubes
  N-dimensional
  Hybrid
  Topology at the level of a node

## Slide 3: Application Characteristics
Computation-bound applications
Communication-heavy applications
  Latency tolerant
  Latency sensitive

## Slide 4: Motivation
Consider a 3D mesh/torus interconnect
Message latencies can be modeled by
(Lf/B) x D + L/B
Lf = length of flit, B = bandwidth,
D = hops, L = message size
When (Lf * D) << L, first term is negligible
But in presence of contention …

## Slide 5: Equidistant-pairs Benchmark
Pair each rank with a partner which is ‘n’ hops away
1 hop
2 hops
3 hops

## Slide 6: Blue Gene/P
7.39 times
Notes: 1 to 2 – 1.84
1 to 3 – 2.11
1 to 4 - 2.55
1 to 7 – 3.54
1 to 8 – 7.396

## Slide 7: Cray XT3
2.23 times
Bhatele A., Kale L. V., Quantifying Network Contention on Large Parallel Machines, Parallel Processing Letters (Special Issue on Large-Scale Parallel Processing), 2009.

## Slide 8: Automatic Mapping Framework
Obtain the processor topology graph and communication graph for the application
Pattern matching to identify 2D/3D/4D near-neighbor communication patterns
Use different heuristics depending on the communication graph
  Structured patterns
  Irregular patterns

## Slide 9: Topology Manager API†
The application needs information such as
  Dimensions of the partition
  Rank to physical co-ordinates and vice-versa
TopoManager: a uniform API
  On BG/L and BG/P: provides a wrapper for system calls
  On XT3/4/5, there are no such system calls
  Provides a clean and uniform interface to the application
† http://charm.cs.uiuc.edu/~bhatele/phd/topomgr.htm
Notes: This can be used by MPI Topology functions

## Slide 10: Object Communication Graph
Obtaining this graph:
  Manually
  Profiling (e.g. IBM’s HPCT tools)
  Charm++’s instrumentation framework
Visualizing the graph
Pattern matching

## Slide 11: WRF Communication Graph
Pattern matching to find out if the communication graph is 2D and what are the dimensions of the graph?
0
1
24
25
26
27
28
29
30
31
0 1 30 31
0
1
31
32

## Slide 12: Mapping Heuristics
Maximum Overlap
Expand from Corners

## Slide 13
Aleliunas, R. and Rosenberg, A. L. On Embedding Rectangular Grids in Square Grids. IEEE Trans. Comput., 31(9):907–913, 1982
Object Graph – 8 x 6
Processor Graph – 12 x 4

## Slide 14: Different mapping heuristics
Bhatele A., Chung I., Kale L. V., Automated Mapping of Structured Communication Graphs onto Mesh Interconnects, in preparation, 2009.

## Slide 15: Evaluation Metric: Hop-bytes
Weighted sum of message sizes where the weights are the number of links traversed by each message
Indication of the communication traffic on the network
Another metric: maximum dilation

## Slide 16
Blue Gene/P (Intrepid)
Cray XT4 (Jaguar)

## Slide 17: Evaluation
Hops 292 292 432 284 236 348
Dilation 11 11 8 7 3 5
Notes: Easily extendable to 3D ?

## Slide 18: Mapping of MPI Applications
Work with IBM (I-Hsin Chung)
  Using HPCT to dump communication patterns
  Derive a mapping offline and use in a subsequent run
Applications: MILC, POP, WRF
  Map 2D communication patterns to 3D tori of BG/P

## Slide 19
Communication graphs for POP and WRF on 256 processors
* FOLD - H. Yu, I.-H. Chung, and J. Moreira. Topology mapping for Blue Gene/L supercomputer. In SC ’06: page 116, New York, NY, USA, 2006.
*
Hops Reduction – 64%
Communication Time Reduction – 45%
Performance Improvement - 17%
Folding of 2D graph to 3D mesh

## Slide 20: OpenAtom Performance on Cray XT3
Chart: No. of cores
| 512 | 1024 | 2048
w256 Default | 7.5 | 5.7 | 3.94
w256 Topology | 6.58 | 4.14 | 2.43
GST_BIG Default | 6.28 | 3.51 | 2.9
GST_BIG Topology | 5.06 | 2.76 | 2.31
Runs on Cray XT3 (Bigben) at Pittsburgh Supercomputing Center, VN mode
(with system reservation to obtain complete 3D mesh shapes)
A. Bhatele, E. Bohm, and L. V. Kale. A Case Study of Communication Optimizations on
3D Mesh Interconnects. In Euro-Par 2009, LNCS 5704, pages 1015–1028, 2009.

## Slide 21: Remaining and Future Work
Consider weighted communication graphs
Mapping of irregular communication graphs
  Unstructured mesh applications, MD codes
Future Work
  Dynamic Load Balancing for MPI applications
  Complex topologies of the future

## Slide 22: I am on the job market …
Acknowledgements:
Prof. Laxmikant V. Kale Prof. David A. Padua
Prof. William D. Gropp Dr. Matthew H. Reilly
IBM Watson Research Center (Blue Gene/L): Fred Mintzer, Glenn Martyna
Pittsburgh Supercomputing Center (Cray XT3): Chad Vizino, Shawn Brown
Argonne National Laboratory (Blue Gene/P): Pete Beckman, Tisha Stacey
Oak Ridge National Laboratory (Cray XT4/5): Donald Frederick, Patrick Worley
Funded in part by the Center for Simulation of Advanced Rockets (Univ. of Illinois) through
DOE Grant B341494
E-mail: bhatele, kale @ illinois.edu Webpage: http://charm.cs.illinois.edu/~bhatele