## Slide 1: Optimizing Molecular Dynamics and Stencil mini-applications for Intel’s Knights Landing
IXPUG, SC’16 Lightning Talk
Kavitha Chandrasekar*, Laxmikant V. Kale
University of Illinois at Urbana Champaign

## Slide 2: Charm++ Runtime System
Supports an asynchronous message-driven execution model
Overdecomposition of work units (or chares) on PEs (Processing Elements)
Migratability of work units
Load balancing framework
Support for several applications
  NAMD
  OpenAtom
  ChaNGa
Charm++ RTS view of over-decomposition
Over-decomposition of work into Charm++ objects
Mapping of Charm++ objects to processors

## Slide 3: LeanMD – Molecular Dynamics Mini-application
Molecular Dynamics simulation application
Atoms in the simulation are divided spatially into k-cells roughly the size of the cutoff distance
  3-away strategy
Uses PINY MD physics engine for its molecular dynamics calculations
Computation bound
  Computation of interacting forces
Communication involved
  Exchange of atoms based on calculated position
Load imbalance from exchange of atoms
Cutoff radius
LeanMD work units

## Slide 4: Stencil3D Application
Five point communication for 2D stencil
Stencil application is representative of communication pattern with neighboring chares in 2D or 3D grid
  Example is MIMD Lattice computation
3D chare array of doubles
Regular communication pattern with 7 neighbor chares
Computation performed on received data
  Temperatures are updated on receiving boundary data from neighbors
Communication/Memory bound
No load imbalance
(x,y)
(x,y+1)
(x+1,y)
(x,y-1)
(x-1,y)

## Slide 5: Experimental Setup
Charm++ in SMP mode
  Reduces message copy
  Ability to map workers to cores
Single KNL node (Stampede 1.5)
  Quadrant mode
  Cache Mode (except for comparison of Cache and Flat mode)
  256 cores were used out of 272 cores for mapping work units to PEs
Performance Tools
  IPC, MCDRAM and DDR4 accesses – perf stat
  Energy numbers – RAPL counters

## Slide 6: LeanMD – Performance Analysis
Load balancing using Greedy heuristics
Speedup (Higher the better)
Energy Usage (Lower the better)
Input size:
  Cell and Compute Dimensions
  16 X 16 X 16 cells
CPU Pinning: No significant degradation was observed without CPU pinning

## Slide 7: Stencil3D - Performance analysis
Large: Stencil3d
  2048 X 2048 X 1024
  Block dimensions: 256 X 128 X 128
Optimal configuration for smaller working set sizes was also observed to be 128 threads (2 hyperthreads per core)
Factors for lack of performance improvement
  Working set size
    Potentially causes increased eviction from MCDRAM
  Higher memory streams in parallel
  Overhead from higher number of worker threads
Scope for energy efficient execution with 2 hyperthreads per core
CPU-pinning: 10%-30% performance degradation without CPU-pinning
  Lack of benefits from L2 locality, context switches, thread migrations
  Load imbalance due to variation in core frequencies

## Slide 8: Flat mode vs. Cache mode
LeanMD and Stencil3D do not show any significant performance difference when run on Cache mode vs Flat mode
Input data size fits in MCDRAM in both cases
Stream is the only benchmark that benefits from Flat mode for input data size half the size of MCDRAM

## Slide 9: Conclusion and Future work
HPC applications like LeanMD and Stencil3D can benefit in terms of performance and energy when tuned appropriately on Knights Landing
  Depending on working set size there might be thrashing of HBM in Cache mode
  Memory bound applications might not benefit from using all 4 hyperthreads
  Overdecomposition factor is a key influencer in performance depending on the number of worker PEs
  Variation in core frequencies can lead to load imbalance making CPU pinning or similar techniques necessary
Automation of tuning for application characteristics within the Charm++ framework by adjusting knobs like
  Hyperthreading
  CPU affinity
  Scheduling on nodes with preferred HBM usage mode