## Slide 1: The Romance and Reality of Task Based Frameworks -Experiences with Uintah
Martin Berzins
Thanks to DOE ASCI (97-10), NSF , DOE NETL+NNSA ARL,NSF , INCITE, XSEDE
www.uintah.utah.edu
Introduction, history, machines
Uintah and its scalability
Tackling Radiative Heat Transfer
Dealing with node performance

## Slide 2
INTRODUCTION,
DAGs, SOFTWARE,
MACHINES, HYPE?
Peak computer power grows by a factor of a thousand every decade and has a profound impact on our ability to undertake science
Often in the past we have had to change our codes…
A very large change is coming as we try to go forward for the next decade.
Are task-based approaches a key technology for this?

## Slide 3: The Exascale challenge for Future Software?
The vision?
Harrod SC12: “today’s bulk synchronous (BSP), distributed memory, execution model is approaching an efficiency, scalability, and power wall.”
The romance ?
Sarkar et al. “Exascale programming will require prioritization of critical-path and non-critical path tasks, adaptive directed acyclic graph scheduling of critical-path tasks, and adaptive rebalancing of all tasks…...”
The reality ???????
“ DAG Task-based programming has always been a bad idea. It was a bad idea when it was introduced and it is a bad idea now “ Parallel Processing Award Winner
Compute
-----------------
Communicate
-----------------
Compute

## Slide 4: Some Historical Background
Ideas go back to 1960s
Vivek Sarkar’s thesis (1989)
  Graphical rep. for parallel programs with cost model (20 procs)
  Compile time cost assignment and schedule
  Macro-data flow for execution
Charm++ Sanjay Kale et al. 1988 onwards. Profound and deep influence
Uintah Steve Parker 1998 onwards (developed independently, starting from SCIRun)
Habanero Java Vivek Sarkar 2007 onwards
Many Recent developments
  CNC, Plasma, Wasatch, ParallelX

## Slide 5: FUTURE MACHINES Energy is the defining issue
Of current approaches, standard cores, many low powered cores and accelerators only hybrid accelerator architectures seem to have exascale potential due to energy requirements
Situation complicated by vertically stacked memory, NVRam, NVlink, poor Xeon Phi KnC and uncertain (KnL KnH) performance
DOE roadmap gives clear plan to 2018
DOE Exascale initiative gives plan to 2024 if funded. NSF? DOD?
Dealing with machine uncertainty part of next decade. Summit 3.5K GPU+P9 nodes. Aurora 50K Intel KnH nodes. ARM?

## Slide 6
INTEL
The basis for next 2 big DOE machines
14nm technology 2016
SCI at Utah is an Intel parallel computing Center

## Slide 7
3D Memory: Stacks DRAM chips into dense modules with wide interfaces, inside the same package as the GPU: several times greater bandwidth, 2X memory capacity 4X energy efficiency.
Unified Memory: allowing the CPU and GPU to access each others memory
NVLink fatter pipe between the CPU and GPU, allowing data flow at > 80GB per second, (16GB per second now).
Size one-third the size of the boards used today,
NVIDIA PASCAL (2016 using 14nm Processes)
20 Gflops per Watt?
BUT ONLY IF YOU CONNECT GPUs TO ARM OR IBM
SCI at Utah is an NVIDIA Cuda Center

## Slide 8: How do we write code that runs on these as well as existing cpu/gpu/phi architectures?
How do we ensure that code persists through the coming architectural changes of the next decade?
“The asynchronous approach on its own is enough isn’t it? “ [DOE Reviewer]
Where are we on the
hype curve?

## Slide 9
Scalability of
Uintah Open Source Software

## Slide 10
* Now at Google
Research team: NSF PetaApps
Qingyu Meng* John Schmidt,, Todd Harman Justin Luitjens*, Jacqueline Beckvermit
Uintah Software Team
* Now at NVIDIA
Phase 1 Uintah software developed 1998-2008 by a team led by Steve Parker
Novel design and reasonable scalability (~1000 cores 2005)
Phase 2 (2008 …)NSF and DOE funded expansion of both scalability and software
PSAAP Extreme Scaling team SANDIA NSFXPS Nan Harish
Alan Humphrey John Holmen Dan Sunderland Brad Peterson Xiao Dasari

## Slide 11
Uintah(X) Architecture
Simulation
Controller
Scheduler
Load
Balancer
Runtime System
ARCHES
DSL: NEBO
WASATCH
PIDX
VisIT
MPM
ICE
UQ DRIVERS
CPUs
GPUs
Xeon Phis
Kokkos Intermediate Layer
Applications code
Programing model
Abstract C++ Task Graph Form
Compilation into C++ Cuda etc
Adaptive Execution of tasks
Intermediate layer for node
Performance on specific cores/processors
Some components have not changed as we have gone from 600 to 600K cores
asynchronous out-of-order execution, work stealing, Overlap communication & computation.

## Slide 12: Uintah Patch, Variables and AMR Outline
ICE is a cell-centered finite volume method for Navier Stokes equations
ICE Structured Grid Variable (for Flows) are Cell Centered Nodes, Face Centered Nodes.
Unstructured Points (for Solids) are MPM Particles
ARCHES is a combustion code using several
different radiation models and linear solvers
Uintah:MD based on Lucretius is a new molecular dynamics component
Structured Grid + Unstructured Points
Patch-based Domain Decomposition
Regular scalable local Adaptive Mesh Refinement
Dynamic Load Balancing
  Profiling + Forecasting Model
  Parallel Space Filling Curves
Works on MPI and/or thread level

## Slide 13
Uintah Directed Acyclic (Task) Graph-Based Computational Framework
Each task defines its computation with required inputs and outputs
Uintah uses this information to create a task graph of computation (nodes) + communication (along edges)
Tasks do not explicitly define communications but only what inputs they need from a data warehouse and which tasks need to execute before each other.
Communication is overlapped with computation
Taskgraph is executed adaptively and sometimes out of order, inputs to tasks are saved
Tasks get data from OLD Data Warehouse and put results into NEW Data Warehouse

## Slide 14: Programing Model for Stencil Computation on a Timestep
Unew = Uold + dt*F(Uold,Uhalo)
Network
Old Data
Warehouse
GET
Uold Uhalo
Halo receives Uhalo
MPI
New Data
Warehouse
PUT
Unew
Halo sends
Example Stencil Task

## Slide 15
The nodal task soup
Task Graph Structure on a Multicore Node with multiple patches
This is not a single graph. Multiscale and Multi-Physics merely add flavor to the “soup”.
There are many adaptive strategies and tricks that are used in the execution of this graph soup.
halos
halos
external
halos
external
halos

## Slide 16: The DAG Approach is not a silver bullet
Uintah Phase 1 1998-2005 – overlap communications with computation. Static task graph execution standard data structures one MPI process per core. No AMR.
Uintah Phase 2 2005-2010 improved fast data structures, load balancer. AMR to 12k cores, then 100K cores using new approach before data structures cause problems.
Out of order and dynamic task execution.
Uintah Phase 3 2010- Hybrid model. Theaded runtine system on node. One MPI process and one data warehouse per node. Multiple cores and GPUs grab tasks as needed. Fast scalable use of hypre for linear equations.
OLD CSAFE
RESULTS 2005
OLD CSAFE
RESULTS
2005

## Slide 17: Uintah Heterogeneous Runtime System (Multiple GPUs and Intel Xeon Phis
Notes: Shared memory model on-node: 1 MPI rank per node - MPI+ Pthreads
Better load-balancing
Decentralized: All threads access task queues and process their own MPI
Scalable, efficient, lock-free data structures

## Slide 18: New Hybrid Model Memory Savings: Ghost Cells
Raw Data: 49152 doubles 31360 doubles
MPI buffer: 28416 doubles 10624 doubles
Total: 75K doubles 40K doubles
MPI:
Thread/MPI:
(example on Kraken, 12 cores/node, 98K core 11% of memory needed
Local Patch
Ghost Cells

## Slide 19
Scalability is at least partially achieved by not executing tasks in order e.g. AMR fluid-structure interaction
Straight line represents given order of tasks Green X shows when a task is actually executed.
Above the line means late execution while below the line means early execution took place. More “late” tasks than “early” ones as e.g.
TASKS: 1 2 3 4 5 1 4 2 3 5
Early
Late execution

## Slide 20: Summary of Uintah Scalability Improvements
Move to a one MPI process per multicore node reduces memory to less than 10% of previous for 100K+ cores
Work on Runtime System involved substantial rewrites
Use optimal size patches to balance overhead and granularity
Use only one data warehouse but allow all cores fast access to it, through the use of atomic operations.
Prioritize tasks with the most external communications
Use out-of-order execution
Algorithm | Random | FCFS | PatchOrder | Most Msg.
Queue Length | 3.11 | 3.16 | 4.05 | 4.29
Wait Time | 18.9 | 18.0 | 7.0 | 2.6
Overall Time | 315.35 | 308.73 | 187.19 | 139.39

## Slide 21: MPM AMR ICE Strong Scaling
*
Complex fluid-structure interaction problem
with adaptive mesh refinement, see SC13/14 paper
NSF funding.
Resolution B
29 Billion particles
4 Billion mesh cells
1.2 Million mesh patches
Mira DOE BG/Q
768K cores
Blue Waters Cray XE6/XK7 700K+ cores

## Slide 22
Deflagration wave moves at ~400m/s not all explosive consumed. Detonation wave moves 8500m/s all explosive consumed.
NSF funded modeling of Spanish Fork Accident 8/10/05
Speeding truck with 8000 explosive boosters each with 2.5-5.5 lbs of explosive overturned and caught fire
Experimental evidence for a transition from deflagration to detonation?

## Slide 23
Spanish Fork Accident
500K mesh patches
1.3 Billion mesh cells
7.8 Billion particles
At every stage when we move
to the next generation of problems
Some of the algorithms and data structures need to be replaced .
Scalability at one level is no certain
Indicator fro problems or machines
An order of magnitude larger

## Slide 24
Utah PSAAP2 Center
Radiative Heat Transfer

## Slide 25: An Exascale Design Problem - Alstom Clean Coal Boiler for 2018 to 2024
For 350MWe boiler problem. LES resolution
needed: 1mm per side for each computational volume = 9x cells
This is one thousand times larger than the largest problems we solve today.
Temperature field
Prof. Phil Smith Dr Jeremy Thornock ICSE

## Slide 26: The team
Computer Science Predictive Modeling Uncertainty Quantification
The Exec

## Slide 27: Existing Simulations of Clean coal Boilers using ARCHES in Uintah
(i) Traditional Lagrangian/RANS approaches do not address well particle effects
(ii) LES has potential to predict oxy--‐coal flames and to be an important design tool
(iii) LES is “like DNS” for coal
Structured, high order finite-volume
Mass, momentum, energy conservation
LES closure
Tabulated chemistry
PDF mixing models
DQMOM (many small linear solves)
Low mach number approx. (pressure Poisson solve up to variables
Radiation via Discrete Ordinates – massive solves or Ray tracing.
Uncertainty quantification
Red is expt
Blue is sim.
Green is consistent

## Slide 28: Radiation: Algorithmic Alternatives
Loose coupling to CFD due to time-scale separation.
  Radiation timescales are typically longer than turbulent mixing timescales.
  Required resolution decreases with distance → AMR.
Discrete Ordinates Method : large linear solves.
RMCRT:
  For optically thin media, this involves all-to-all coupling but no linear solve
  AMR is a natural fit.
    Phenomena nearby have a greater effect than phenomena at a distance.
    Coarse representation of nonlocal features
Global replication of semi-coarsened form of global radiation mesh on each node – gives a local calculation

## Slide 29: Radiation Overview
Solving energy and radiative heat transfer equations simultaneously
  Radiation-energy coupling incorporated by radiative source term
  Energy equation conventionally solved by ARCHES (finite volume)
  Temperature field, T used to compute net radiative source term
  requires integration of incoming intensity about a sphere
Diffusion – Convection + Source/Sinks
Global replication of semi-coarsened form of global radiation mesh on each node – gives a local calculation
Notes: The net radiative source term consists of two terms, one of which requires integration of incoming intensity about a sphere
RMCRT approximates the second term using Monte-Carlo methods

## Slide 30: Reverse Monte Carlo Ray Tracing
Incorporate dominant physics
  Emitting / Absorbing Media
  Emitting and Reflective Walls
  Ray Scattering
User controls # rays per cell
  Each cell has Temp Absorb and Scattering Coeffs
Radiative Heat Transfer key
  Replicate Geometry on every node
  Calculate heat fluxes on Geometry
  Transfer cell info e.g etc from all nodes to all nodes
Reverse ray tracing back from
Heat flux at walls to origin
More efficient than forward ray tracing
Notes: Virtual Radiometer - Computationally mimics an experimental heat flux sensor. - Allows for direct comparison with experimental results, validation - Easy to implement inside of RMCRT, very difficult in DOM. - User can place VR anyplace in the flow at any orientation

## Slide 31: RMCRT Compute Nodes and Mesh Notation
  Original global mesh Nnode each with Npatches x (Npoints)^3
Now Coarse mesh Nnode each with Npatches x (Npoints/Nrefine)^3
Each node has its own fine mesh + fine mesh
halos and a global coarse mesh
Radiative properties for each node need to be updated
for every radiation calculation. each processor shares the temperature and radiative-properties fields (absorption
coefficients, scattering coefficients, and cell types) with all
other processors.
Global all to all on coarse mesh Local halo fine mesh updates

## Slide 32
Strong Scaling Results for RMCRT on Titan

## Slide 33
Communications Volume: Number of Messages in Strong Scaling
Cores / Mesh size | 128 | 256 | 512 | 1K | 4K | 8K | 16K | 32K | 64K | 128K
128^3 | 377 | 1K | 3K | 6K | 36K |  |  |  |  | 
256^3 |  |  |  | 9K | 52K | 105K | 212K | 437K |  | 
512^3 |  |  |  |  |  | 340K | 670K | 1.4M | 2.7M | 5.4M
How much volume can the communications network take?

## Slide 34: GPU Single Mesh Scaling

## Slide 35: Current Efforts on porting RMCRT to Xeon Phi
Native execution experiments have explored :
  optimal run configurations
  use of the 61st (reserved) core on the Xeon Phi
  thread affinity
  mesh decomposition
Key Outcomes:
  two Xeon E5s outperformed one Xeon Phi by 40%
  mesh decomposition had a profound impact on performance
  No one thread placement strategy dominated performance
  Differing caches of Sandy Bridge and MIC matter
  Simple vectorization approaches failed (e.g. SIMD directives)
  Many options are available to explore (e.g. manual intrinsics and software packages such as Kokkos (SNL) or RAJA (LLNL))
  Complete code overhaul necessary

## Slide 36
Native execution of single-level RMCRT on a single coprocessor
Target impact of thread affinity, thread count, and patch size on performance
Key Takeaways
  The Xeon E5 outperformed the Xeon Phi by about 40%
  No one thread placement strategy and/or thread count best
  Thread affinity during coprocessor-side experiments was on par with that of Xeon
Challenge
  Domain decomposition and coprocessor-based memory footprint restrictions
Initial Radiation Experiments on INTEL Xeon PHI
No use of AVX vector instructions yet
CPU
Xeon Phi

## Slide 37: Portability and Node Performance
Even if we scale can we get both portability and performance at node level?
Use Domain Specific Language
Or use abstraction layer that maps loops onto machine efficiently (e.g. Kokkos Rajah)

## Slide 38: NEBO/Wasatch Example
Energy equation
Enthalpy diffusive flux
Dependency
specification
Execution
order
Express complex pde functions as DAG - automatically construct algorithms from expressions
Define field operations needed to execute tasks (fine grained vector parallelism on the mesh)
User writes only field operations code . Supports field & stencil operations directly - no loops!
Strongly typed fields ensure valid operations at compile time. Allows implementations to be tried without modifying application code.
Scalability on a node - use Uintah infrastructure to get scalability across whole system
[Sutherland Earl Might]

## Slide 39: GPU Task and Data Management
Use CUDA Asynchronous API
Automatically generate CUDA streams for task dependencies
Concurrently execute kernels and memory copies
Preload data before task kernel executes
Multi-GPU support
hostComputes
hostRequires
existing host memory
devComputes
devRequires
Pin this memory with CudaHostRegister()
Page locked buffer
cudaMemcpyAsync(H2D)
computation
cudaMemcpyAsync(D2H)
Free pinned host memory
Result back on host
Call-back executed here
(kernel run)
Automatic D2H copy here
Framework Manages Data Movement
Host   Device
Data Transfer
Kernel Execution
Kernel Execution
Data Transfer
Normal
Page-locked Memory
Notes: With Uintah’s knowledge of the task-graph, task data is automatically transferred asynchronously to the device before a GPU task executes
Stream - sequence of operations that execute in order on GPU
  Operations from different streams can be interleaved

## Slide 40
Keeping Data on the GPU
  New GPU engine can now keep data resident on the GPU, avoiding unnecessary PCIe bus data transfers and automatically handles ghost/halo cells across multiple CPU threads, multiple GPUs per node, and multiple nodes.
Poisson Problem | Problem Size | Number of Patches | Avg Time Per Iteration
CPU engine (Xeon 12 cores) | 400x400x400 | 12 (3x2x2) | 0.653
Current GPU engine (K20) | 400x400x400 | 12 (3x2x2) | 0.344
New GPU engine (K20) | 400x400x400 | 2 (1x1x2) | 0.098

## Slide 41
Consolidating GPU Data Transfers
  Current GPU scheduler performs a cudaMalloc and a cudaMemcpy for each variable per patch per material. For some tasks, hundreds of pieces of variable data needed to be copied, and the slowdown of these API calls is severe.
  The new GPU scheduler's support for consolidating data is nearing completion. Early results show fewer API calls.

## Slide 42: DESIGNING FOR EXASCALE
Clear trend towards accelerators e.g. GPU but also Intel MIC – NSF “Stampede” Balance factor = flops/bandwidth – high.PORTABILITY IS THE KEY ISSUE:NEW CODE - use Wasatch to generate code for GPUs and MICs .How do we handle the challenge of existing code?
Standard C++, Not a language extension
  In spirit of TBB, Thrust & CUSP, C++AMP, LLNL’s RAJA, ...
  Not a language extension like OpenMP, OpenACC, OpenCL, CUDA, ...
Uses C++ template meta-programming
Multidimensional Arrays, with a twist
  Layout mapping: multi-index (i,j,k,...)  memory location
  Choose layout to satisfy device-specific memory access pattern
  Layout changes are invisible to the user code
Kokkos: A Layered Collection of Libraries
[source Carter Edwards and Dan Sunderland]

## Slide 43: Evaluate Performance Impact of Array Layout [Edwards and Sunderland]
Molecular dynamics computational kernel in miniMD
Simple Lennard Jones force model:
Atom neighbor list to avoid N2 computations
  Test Problem
  864k atoms, ~77 neighbors
  2D neighbor array
    Different layouts CPU vs GPU
  Random read ‘pos’ through
  GPU texture cache
Large performance loss
with wrong array layout
pos_i = pos(i);
for( jj = 0; jj < num_neighbors(i); jj++) {
j = neighbors(i,jj);
r_ij = pos_i – pos(j); //random read 3 floats for pos
if (|r_ij| < r_cut) f_i += 6*e*((s/r_ij)^7 – 2*(s/r_ij)^13)
}
f(i) = f_i;
Chart: GFlop/s
| Xeon | Xeon Phi | K20x
wrong layout (with texture) | 24.4771 | 13.223 | 25.45
correct layout (without texture) | 21.1596
correct layout (with texture) | 22.3118 | 32.1693 | 122.3503

## Slide 44
Sandia (Bennett) Evaluation of Uintah /Legion/Charm++ on MiniAero MiniApp
  2 Day integration/porting effort Utah/Sandia (12/14).
  Rewrite using Uintah constructs
  MiniAero is a new Uintah component -Uintah & DOE developers are contributing to code base
  In 7 days, 90% of the core features working within Uintah .
  Uintah- MiniAero scales “out of the box” to 131K cores on Titan.
  Further scaling/tuning by Sandia
  Uintah software development
  Motivation Uintah team to improve documentation etc
Todd Harman, Alan Humphrey
Dav de St Germain John Schmidt

## Slide 45: Summary
Layered DAG abstraction important for portability, scaling and for not needing to change applications code
Scalability still requires tuning the runtime system. Cannot develop nodal code in isolation.
Future Portability: use Kokkos for rewriting legacy applications +Wasach/Nebo DSL for new code. MIC and GPU ongoing. Aiming at future DOE machines Summit and Aurora.
Linear Solvers Hypre and AMGX ? Trilinos Petsc?

## Slide 46: Backup slides

## Slide 47
Runtime System

## Slide 48: Existing Simulations of Boilers using ARCHES in Uintah
(i) Traditional Lagrangian/RANS approaches do not address well particle effects
(ii) LES has potential to predict oxy--‐coal flames and to be an important design tool
(iii) LES is “like DNS” for coal, but 1mm mesh needed to capture key phenomena
Mesh spacing filter

## Slide 49
Each Mira Run is scaled wrt the Titan Run at 256 cores
Note these times are not the same for different patch sizes.
2.2 Trillion
DOF
Weak Scalability of Hypre Code
Linear Solves arises from Low Mach Number Navier –Stokes Equations
Use Hypre Solver from LLNL
Preconditioned Conjugate Gradients on regular mesh patches used
Multi-grid pre-conditioner used
Careful adaptive strategies needed to get scalability
One radiation solve
every 10 timesteps

## Slide 50
Strong Scaling of AMR Algorithms
– problem size fixed as number of cores increases
should lead to decreasing execution time.
Dots are data and lines are models
T: GBRv1 = c1 (Flags/Proc) log(npatches ) + c2 M(GBRv1)
T: Tiled = c5 Nmeshcells / Proc
T: LBR = GBR on a compute node
No strong scaling
Strong Scaling
GBR is Global
Berger-Rigoutsos

## Slide 51: Burgers Example I
<Grid>
<Level>
<Box label = "1">
<lower> [0,0,0] </lower>
<upper> [1.0,1.0,1.0] </upper>
<resolution> [50,50,50] </resolution>
<patches> [2,2,2] </patches>
<extraCells> [1,1,1] </extraCells>
</Box>
</Level>
</Grid>
void Burger::scheduleTimeAdvance( const LevelP& level,
SchedulerP& sched)
{
…..
task->requires(Task::OldDW, u_label, Ghost::AroundNodes, 1);
task->requires(Task::OldDW, sharedState_->get_delt_label());
task->computes(u_label);
sched->addTask(task, level->eachPatch(), sharedState_->allMaterials());
}
25 cubed patches
8 patches
One level of halos
Get old solution from old data warehouse
One level of halos
Compute new solution

## Slide 52: Burgers Equation code
void Burger::timeAdvance(const ProcessorGroup*, const PatchSubset* patches,
const MaterialSubset* matls, DataWarehouse* old_dw, DataWarehouse* new_dw)
//Loop for all patches on this processor
{ for(int p=0;p<patches->size();p++){
//Get data from data warehouse including 1 layer of "ghost" nodes from surrounding patches
old_dw->get(u, lb_->u, matl, patch, Ghost::AroundNodes, 1);
// dt, dx Time and space increments
Vector dx = patch->getLevel()->dCell();
old_dw->get(dt, sharedState_->get_delt_label());
// allocate memory for results new_u
new_dw->allocateAndPut(new_u, lb_->u, matl, patch);
// define iterator range l and h …… lots missing here and Iterate through all the nodes
for(NodeIterator iter(l, h);!iter.done(); iter++){
IntVector n = *iter;
double dudx = (u[n+IntVector(1,0,0)] - u[n-IntVector(1,0,0)]) /(2.0 * dx.x());
double du = - u[n] * dt * (dudx);
new_u[n]= u[n] + du;
}

## Slide 53
Task Compile
Run Time
(each timestep)
xml
Parallel I/O
UINTAH ARCHITECTURE
Calculate Residuals
Solve Equations
RUNTIME SYSTEM
Visus PIDX
VisIt
ARCHES or WASATCH/NEBO

## Slide 54: RMCRT Computational Complexity
abskg: (double) absorption coefficient - property of the medium ray travels through.
sigmaT4: (double) physical constant, (sigma)) * T ^ 4
divQ: (double) divergence of the heat flux in and out of each computational cell
cellType (int) flag to indicate type of cell
Communication:
( (abskg + sigmaT4 + cellType) * DomainSize for each patch )
Computation cost per patch
= C1 * #rays * (#cells ^ 1.4)
Doubling resolution from
32^3-> 64^3, the cost goes up
by a factor of 20.

## Slide 55: Radiation: Algorithmic Alternatives
Loose coupling to CFD due to time-scale separation.
  Radiation timescales are typically longer than turbulent mixing timescales.
  Required resolution decreases with distance → AMR.
Discrete Ordinates Method : large linear solves.
RMCRT:
  For optically thin media, this involves all-to-all coupling but no linear solve
  AMR is a natural fit.
    Phenomena nearby have a greater effect than phenomena at a distance.
    Coarse representation of nonlocal features

## Slide 56: Task prioritization algorithms
Algorithm | Random | FCFS | PatchOrder | MostMsg.
Queue Length | 3.11 | 3.16 | 4.05 | 4.29
Wait Time | 18.9 | 18.0 | 7.0 | 2.6
Overall Time | 315.35 | 308.73 | 187.19 | 139.39
Task pool
to be executed
MPI sends
Sub-domain
Prioritize tasks with external communications over purely internal ones
Executing the task pool in different ways leads to different communications patterns

## Slide 57: Granularity Effect
Decrease patch size
  (+) Increase queue length
  (+) More overlap, lower task wait time
  (+) More patches, better load balance
  (-) More MPI messages
  (-) More regrid overheads
Other Factors
  Problem size
  Implied task level parallelism
  Interconnection bandwidth and legacy
  CPU cache size
Solution- Self Tuning?

## Slide 58: Intel Xeon Phi
Adoption of Intel’s MIC Architecture in large-scale HPC infrastructures is increasing
Uintah MUST be capable of leveraging this adoption
Xeon Phi Knight’s Corner MIC Architecture
  Up to 61 cores, 244 threads
  Up to 1208 GFLOPS peak
  Up to 352 GB/s peak memory bandwidth 8 GB or 16 GB GDDR5 memory
  512-bit SIMD instructions
Intel Xeon Phi Coprocessor Core Architecture
John Holmen

## Slide 59
NVIDIA K20m GPU ~order of magnitude speedup over
16 CPU cores
(Intel Xeon E5-2660 @2.20 GHz)
K20 and K40
Internal 200- 300 GB/sec
External 8-16 GB/sec (the Dixie straw)